## Slide 1
FreeSurfer Introduction

## Slide 2
Course Overview
Day 1
  Introduction
  Individual Subject Analysis
  Troubleshooting
Day 2
  ROI Analysis
  Surface-based Analysis
  Group Analysis
  Longitudinal Analysis

## Slide 3
Course Schedule Day 1
https://surfer.nmr.mgh.harvard.edu/fswiki/VirtualCourse#preview
Notes: -click on the links on the schedule page to access the slides to follow along & to access the tutorials when it’s time to do those

## Slide 4
Course Schedule Day 2
https://surfer.nmr.mgh.harvard.edu/fswiki/VirtualCourse#preview
Notes: -click on the links on the schedule page to access the slides to follow along & to access the tutorials when it’s time to do those

## Slide 5
Lectures and Practicals
General format: talk followed by tutorial
Search on YouTube for the FreeSurfer channel!
Note about tutorials: we have many people with different background who will help. Whoever comes over first will either be able to answer your question(s), or will find someone who can
Notes: -Our staff will be in the room during tutorials; raise your hand to get their attention
-We have many people with different background who will help. Whoever comes over first will either be able to answer your question(s), or will find someone who can.

## Slide 6
Post Your Questions!
http://surfer.nmr.mgh.harvard.edu/cgi-bin/fsurfer/questions.cgi

## Slide 7
Search for Answers

## Slide 8
Spatial
Normalization
Surface
Extraction
Individual T1
Surface Mesh
Curvature
Inflation
Sphere
Group
Template
Thickness
(Group Space)
Statistical Map
Statistical Map
Smooth
p<.01
p<.01
Thickness
2mm
4mm
Deformation
Field
Apply
Deformation
Group
Analysis
A
G
A
D
C
B
J
I
H
F
E
M
L
K
N
O
What Is FreeSurfer?
Surface ROI
Volume ROI
Other Subjects

## Slide 9
What is FreeSurfer?
Total # licenses distributed as of June 9, 2023
(65631 total)

## Slide 10
Outline
A Brief History of FreeSurfer
What are Surfaces Good For Anyway?
Inferring Microstructural Locations
Longitudinal Analysis
DWI/Tractography
fMRI

## Slide 11: FreeSurfer began life as a means for EEG/MEG Analysis
Improved localization of cortical activity by combining EEG and MEG with MRI cortical surface reconstruction: a linear approach. AM Dale, MI Sereno. Journal of cognitive neuroscience 5 (2), 162-176, 1994.
Dynamic statistical parametric mapping: combining fMRI and MEG for high-resolution imaging of cortical activity. AM Dale, AK Liu, et al, Neuron 26 (1), 55-67, 2000.
Citations
2298
1749

## Slide 12: How To Model The Pial Surface? (an unanswered question circa 1996)

## Slide 13: Inferring the Location of the Pial Surface
Cortical surface-based analysis: I. Segmentation and surface reconstruction. AM Dale, B Fischl, MI Sereno, Neuroimage 9 (2), 179-194. 1999.
Cortical surface-based analysis: II: inflation, flattening, and a surface-based coordinate system. B Fischl, MI Sereno, AM Dale Neuroimage 9 (2), 195-207. 1999.
Citations
9641
6093
Key Insight (Anders’ and Marty’s, not mine): Model the gray/white boundary and use it to infer pial surface locations

## Slide 14: Inferring the Location of the Pial Surface
Cortical surface-based analysis: I. Segmentation and surface reconstruction. AM Dale, B Fischl, MI Sereno, Neuroimage 9 (2), 179-194. 1999.
Cortical surface-based analysis: II: inflation, flattening, and a surface-based coordinate system. B Fischl, MI Sereno, AM Dale Neuroimage 9 (2), 195-207. 1999.
My Favorite Review: “In the method section alone, scholarship is lacking, the notation is incorrect and misleading and even a basic understanding of elementary topology is lacking…
Citations
9641
6093
Key Insight (Anders’ and Marty’s, not mine): Model the gray/white boundary and use it to infer pial surface locations

## Slide 15: Inferring the Location of the Pial Surface
Cortical surface-based analysis: I. Segmentation and surface reconstruction. AM Dale, B Fischl, MI Sereno, Neuroimage 9 (2), 179-194. 1999.
Cortical surface-based analysis: II: inflation, flattening, and a surface-based coordinate system. B Fischl, MI Sereno, AM Dale Neuroimage 9 (2), 195-207. 1999.
That said, this is by far the strongest section of the paper”
My Favorite Review: “In the method section alone, scholarship is lacking, the notation is incorrect and misleading and even a basic understanding of elementary topology is lacking…
Citations
9641
6093
Key Insight (Anders’ and Marty’s, not mine): Model the gray/white boundary and use it to infer pial surface locations

## Slide 16: FreeSurfer: Surface-based modeling challenges
One wants a topologically correct model (no handles or holes) so that (1) distances along the surface aren’t dramatically distorted, and (2) it is possible to establish point-to-point registration across subjects for every point in the cortex, but….
The only technique to guarantee topology at the time was “shrink wrapping” in which you start with a surface of the correct topology (a sphere) and try to deform it so it settles on the true pial surface.
The problem is that shrink wrapping a highly-folded surface like the human brain is HARD!*.
*We have made some Deep Learning progress on this. See (Hoopes et al., MIDL 2022 ):
https://openreview.net/forum?id=-JiHeZNDY3a

## Slide 17: How To Get The Topology Right?

## Slide 18: Why Shrink wrapping is Hard!

## Slide 19: Shrink Wrapping

## Slide 20: Topology Correction

## Slide 21
Topological defect
Corrected defect
Initial cortical surface
Sagittal view
Coronal view
Automatic Defect Correction

## Slide 22: Topology Correction via Manifold Surgery
BEFORE
AFTER

## Slide 23
Subject 1
Subject 2 aligned with Subject 1
(Subject 1’s Surface)
Problems with Affine (12 DOF) Registration

## Slide 24
A Surface-Based Registration
Common space for group analysis (like Talairach) “fsaverage”

## Slide 25: Topology Correction and Spherical Averaging
High-resolution intersubject averaging and a coordinate system for the cortical surface. B Fischl, MI Sereno, RBH Tootell, AM Dale. Human brain mapping 8 (4), 272-284, 1999.
Automated manifold surgery: constructing geometrically accurate and topologically correct models of the human cerebral cortex. B Fischl, A Liu, AM Dale, IEEE transactions on medical imaging 20 (1), 70-80, 2001.
Citations
3068
1726
My Second Favorite Review. We intended to submit equations like:

## Slide 26: Topology Correction and Spherical Averaging
High-resolution intersubject averaging and a coordinate system for the cortical surface. B Fischl, MI Sereno, RBH Tootell, AM Dale. Human brain mapping 8 (4), 272-284, 1999.
Automated manifold surgery: constructing geometrically accurate and topologically correct models of the human cerebral cortex. B Fischl, A Liu, AM Dale, IEEE transactions on medical imaging 20 (1), 70-80, 2001.
My Second Favorite Review. Incorrect printer fonts turned them into:
 = ♠♣♥♦
Citations
2260
1212

## Slide 27: Topology Correction and Spherical Averaging
High-resolution intersubject averaging and a coordinate system for the cortical surface. B Fischl, MI Sereno, RBH Tootell, AM Dale. Human brain mapping 8 (4), 272-284, 1999.
Automated manifold surgery: constructing geometrically accurate and topologically correct models of the human cerebral cortex. B Fischl, A Liu, AM Dale, IEEE transactions on medical imaging 20 (1), 70-80, 2001.
My Second Favorite Review: “”
 = ♠♣♥♦
Citations
2260
1212

## Slide 28: And Finally, the Aseg
Whole brain segmentation: automated labeling of neuroanatomical structures in the human brain. B Fischl, DH Salat, et al., Neuron 33 (3), 341-355. 2002
Sequence-independent segmentation of magnetic resonance images. B Fischl, DH Salat, et al., Neuroimage 23, S69-S84, 2004.
Citations
7703
2055
Caudate
Pallidum
Putamen
Amygdala
Hippocampus
Lateral Ventricle
Thalamus
White Matter
Cortex
The aseg was the final piece that let us totally automate the processing.

## Slide 29
Outline
A Brief History of FreeSurfer
What are Surfaces Good For Anyway?
Inferring Microstructural Features
Longitudinal Analysis
DWI/Tractography
fMRI

## Slide 30
What Can One Do With A Surface Model?
left primary visual cortex
right visual
hemifield
desired shape of activity pattern
required shape of stimulus
goal: use model to imposed desired activity pattern on V1
Collaboration with Jon Polimeni and Larry Wald.
w=k log(z+a)

## Slide 31
Tangential Resolution Measured with Surface-based Analysis
Collaboration with Jon Polimeni and Larry Wald. Polimeni, et al, 2010, NI.

## Slide 32
Tangential Resolution Measured with Surface-based Analysis
Collaboration with Jon Polimeni and Larry Wald. Polimeni, et al, 2010, NI.

## Slide 33
NeuroMarketing!
Thanks to Larry Wald for this slide.
Aim 1 of our NCRR Center Grant, spelling:
“MGH Center for Functional Neuroimaging Technologies; and NCRR Center for Research Resources.”
(just kidding)

## Slide 34
Outline
A Brief History of FreeSurfer
What are Surfaces Good For Anyway?
Inferring Microstructural Locations
Longitudinal Analysis
DWI/Tractography
fMRI

## Slide 35
Surface-based Registration Performance
Brodmann, 1909

## Slide 36
Predicting Brodmann Areas: Talairach Coordinates
BA17 (V1) BA18 (V2) BA44 (Broca’s) BA45 (Broca’s)
1 subject overlap
10 subjects overlap
(Amunts et al, 2000, 2004)

## Slide 37
Predicting Brodmann Areas from Folding Patterns
Fischl, et al, 2007. Thanks to Katrin Amunts, Karl Zilles and Hartmut Mohlberg for the data, and to Niranjini Rajendran and Evelina Busa for the analysis.
BA 44
BA 45
BA 18 (V2)
BA 17 (V1)
100% Overlap
0%

## Slide 38
Ex vivo MRI of hippocampal subfields
Resolution as high as 0.1 mm isotropic
Allows precise manual tracing of hippocampal subfields.
The delineation only relies on geometry for subdividing the CA.
Joint work with J. Eugenio Iglesias, Koen van Leemput and Jean Augustinack
Notes: 38

## Slide 39
Automated Segmentation
We use the atlas as a prior, and connect it to the image through a Gaussian likelihood term for each label.
This makes the segmentation sequence-independent.
0.6 mm isotropic T1 (Winterburn et al.) 1 mm T1 + 0.4x0.4x2 mm T2 (ADNI)
Joint work with J. Eugenio Iglesias, Koen van Leemput and Jean Augustinack
Notes: 39

## Slide 40
Outline
A Brief History of FreeSurfer
What are Surfaces Good For Anyway?
Inferring Microstructural Locations
Longitudinal Analysis
DWI/Tractography
fMRI

## Slide 41
Robust Registration
Reuter et al, 2010 NeuroImage
Target
Target

## Slide 42
Robust Registration
Reuter et al, 2010 NeuroImage
Registered Src correlation ratio
Registered Src Robust

## Slide 43
Tumor data with significant intensity differences in the
brain, registered to first time point (left).
Robust Registration
Reuter et al, 2010 NeuroImage

## Slide 44
Create unbiased subject template (iterative registration to median)
Process template
Initialize time points
Let it evolve there
Avoid Bias: All time points are treated the same
Increases sensitivity and reliability!
Longitudinal Processing
Reuter et al. OHBM 2010, NeuroImage 2011 & 2012

## Slide 45
Outline
A Brief History of FreeSurfer
What are Surfaces Good For Anyway?
Inferring Microstructural Locations
Longitudinal Analysis
DWI/Tractography
fMRI

## Slide 46
Tractography with TRACULA (TRActs Constrained by the Underlying Anatomy)
Collaboration with Anastasia Yendiki, Lilla Zöllei, Saad Jbabdi, Tim Behrens and Jean Augustinack
Completely automated modeling of 18 major fascicles
Uses prior probabilistic information on the anatomical structures that each fascicle goes through or next to

## Slide 47
Outline
A Brief History of FreeSurfer
What are Surfaces Good For Anyway?
Inferring Microstructural Locations
Longitudinal Analysis
DWI/Tractography
fMRI

## Slide 48
15 sec ‘ON’, 15 sec ‘OFF’
Flickering Checkerboard
Auditory Tone
Finger Tapping
Sampling on the Surface

## Slide 49
fMRI Working Memory Paradigm Group Analysis
Probe-vs-Fixation. Data Functional Biomedical Informatics Research Network (fBIRN)

## Slide 50
Spatial Smoothing
5 mm apart in 3D
25 mm apart on surface!
Kernel much larger
Averaging with other tissue types (WM, CSF)
Averaging with other functional areas

## Slide 51
Group fMRI Analysis: Volume vs Surface
Affine registration to MNI305
5mm volume smoothing vs.
10mm surface smoothing

## Slide 52
What is FreeSurfer?
Cortical extraction and labeling
Subcortical Segmentation
Surface-based Inter-subject Registration
Fully automated
Multi-modal integration
Use FreeSurfer
Be Happy

## Slide 53: Why Should I Use FreeSurfer?
Please do not try this yourself without expert supervision – it can be extremely dangerous!

## Slide 55
Food and such
Morning coffee and “breakfast” – muffins, bagels, fruit
Afternoon coffee and some snacks
Tuesday evening socializing at Boston Beer Works
Cafeteria in main building (Building 149)

## Slide 56
To Caffeinate or not to Caffeinate?
Please don’t spill coffee (or anything else!) on the laptops. If you do, please be prepared to fund a replacement!

## Slide 57
The FreeSurfer Team
57
Bruce
Doug
fMRI/PET
Martin
Longitudinal
Anastasia
Tractography
Lilla
Registration/
Pediatric
Zeke
Software Engineers
Ruopeng
Nick
Andre
MR Sequences
Allison
Recon Editing & Exvivo Data
Notes: -Bruce: creator, implements most new code
-Doug: created & only person that works on fMRI stream; person that mostly works on group analysis code
-engineers: build & test the code; decide when to release new versions; most likely to help with installation problems
-me: expertise in manual interventions for failed datasets; oversee exvivo projects that ultimately add to atlases

## Slide 58
Automated Subfield Segmentation
high-resolution scan
of unseen subject
automated labeling
manual labeling
Leave-one-out cross-validation with 5 subjects
Collaboration with Koen van Leemput, J. Eugenio Iglesias and Jean Augustinack
Dice Coefficient
Relative Volume Difference (%)
Fimbria
CA2/3
CA1
CA4/DG
Presubiculum
Subiculum
Hippocampal fissure
Hippocampus
Inf. Lateral Ventricle
Choroid plexus
.8
.7
.6
.5
.4
.3
.2
.1
0
80
70
60
50
40
30
20
10
0
27

## Slide 59
33
Visual/Auditory/Motor Activation Paradigm
15 sec ‘ON’, 15 sec ‘OFF’
Flickering Checkerboard
Auditory Tone
Finger Tapping

## Slide 60
34
On-vs-Off SPMs
+3%
0%
-3%
Contrast Amplitude
CON, COPE, CES
Contrast Amplitude
Variance
(Error Bars)
VARCOPE, CESVAR
Significance
t-Map (p,z,F)
(Thresholded p<.01)

## Slide 61
42
Outline
Anatomical Analysis
Surface-based (Cortex)
Volume-based
Multi-modal integration
DWI/Tractography
fMRI – retinotopy

## Slide 62
43
What does your brain do to Mona?

## Slide 63
44
Left Cortical
Hemisphere
Right Cortical
Hemisphere

## Slide 64
45
HM
VML
VMU
HM – Horizontal Meridian
VML – Vertical Meridian, Lower Field
VMU – Vertical Meridian, Upper Field
Cortex
Cartesian
Map Function
log(k(x+iy)+a)

## Slide 65
46
V1 – Primary Visual Cortex
HM
VMU
VML

## Slide 66
47
Retinotopic fMRI
Ring (Exp/Con)
(Eccentricity)
Wedge (Rot)
(Azimuth)

## Slide 67
48
Retinotopic fMRI Analysis
β1=Asin(R)
β2=Acos(R)
Rtan (β1/β2)
-1
R
Eccentricity
REccentricity Radius

## Slide 68
49
Azimuth
Eccentricity
Isoclines
Eccentricity
Azimuth
Polimeni, NI 2010
Retinotopy Results

## Slide 69
39
Spatial
Normalization
Surface
Extraction
Individual T1
Surface Mesh
Curvature
Inflation
Sphere
Group
Template
Thickness
(Group Space)
Statistical Map
Statistical Map
Smooth
p<.01
p<.01
Thickness
2mm
4mm
Deformation
Field
Apply
Deformation
Group
Analysis
A
G
A
D
C
B
J
I
H
F
E
M
L
K
N
O
FreeSurfer Analysis Pipeline Overview
Surface ROI
Volume ROI
Other Subjects

## Slide 70
54
Spatial
Normalization
Surface
Extraction
Individual T1
Surface Mesh
Curvature
Inflation
Sphere
Group
Template
Thickness
(Group Space)
Statistical Map
Statistical Map
Smooth
p<.01
p<.01
Thickness
2mm
4mm
Deformation
Field
Apply
Deformation
Group
Analysis
A
G
A
D
C
B
J
I
H
F
E
M
L
K
N
O
FreeSurfer Analysis Pipeline Overview
Surface ROI
Volume ROI
Other Subjects

## Slide 71
55
Quantifying Folding Patterns
Height or Depth Encodes Folding Pattern
Every vertex has a value
Central Sulcus
Gyri
Sulci
Central Sulcus

## Slide 72
56
Motivation
To a large degree, function follows the folding patterns. So if you align the folding patterns between two subjects you will align the function.

## Slide 73
57
Intersubject Registration
Subject 1
Central Sulcus
Subject 2
Central Sulcus
Central Sulcus

## Slide 74
58
Surface Registration
Subject 1
Subject 2 (Before)
Subject 2 (After)
Shift, Rotate, Stretch
High dimensional (~500k)

## Slide 75
59
What Can One Do With A Surface Model?
left primary visual cortex
right visual
hemifield
desired shape of activity pattern
required shape of stimulus
goal: use model to imposed desired activity pattern on V1
Collaboration with Jon Polimeni and Larry Wald.
w=k log(z+a)

## Slide 76
76
Use FreeSurfer
Be Happy
Thanks!

## Slide 77
From (Sereno et al, 1995, Science).
Retinotopy Field Sign Maps
Changes in orientation between V1, V2, etc

## Slide 78
62
Surface Review
Cortex is a 2D sheet folded into 3D
Function is organized along the sheet
Visualization
Better to smooth in 2D instead of 3D
Register across subjects by aligning anatomy (folding patterns) in 2D
Common surface space (like Talairach) for group studies

## Slide 79
63
Surface Registration
Subject 1
Subject 2 (Before)
Subject 2 (After)

## Slide 80
Surfaces: White and Pial

## Slide 81
Surface and Volume Analysis
Cortical Reconstruction
and Automatic Labeling
Inflation and Functional
Mapping
Surface Flattening
Surface-based Intersubject
Alignment and Statistics
Automatic Subcortical
Gray Matter Labeling
Automatic Gyral White
Matter Labeling

## Slide 82
Inflation

## Slide 83
Inflated surface with cuts
superior temporal
Metrically optimal flat map
calcarine
central
sylvian
anterior
posterior
Surface Flattening – Whole Hemisphere

## Slide 84
Volume Differences Predictive of AD
Data courtesy of Drs Marilyn Albert and Ron Killiany

## Slide 85
Why FreeSurfer?
Anatomical analysis is not like functional analysis – it is completely stereotyped.
Registration to a template (e.g. MNI/Talairach) doesn’t account for individual anatomy.
Even if you don’t care about the anatomy, anatomical models allow functional analysis not otherwise possible.

## Slide 86
ICBM Atlas
Why not just register to an ROI Atlas?
12 DOF
(Affine)

## Slide 87
Subject 1
Subject 2 aligned with Subject 1
(Subject 1’s Surface)
Problems with Affine (12 DOF) Registration

## Slide 88
Talk Outline
Cortical (surface-based) Analysis.
Volume Analysis.
New Features in 5.1.

## Slide 89
What Can One Do With A Surface Model?
left primary visual cortex
right visual hemifield
desired shape of activity pattern
required shape of stimulus
goal: use model to imposed desired activity pattern on V1
Collaboration with Jon Polimeni and Larry Wald.
w=k log(z+a)

## Slide 90
Tangential Resolution Measured with Surface-based Analysis
Collaboration with Jon Polimeni and Larry Wald.

## Slide 91
Tangential Resolution Measured with Surface-based Analysis
Collaboration with Jon Polimeni and Larry Wald.

## Slide 92
Cortical Thickness
white/gray surface
pial surface
lh.thickness, rh.thickness
Distance between white and pial surfaces
One value per vertex

## Slide 93
A Surface-Based Coordinate System

## Slide 94
Inter-Subject Averaging
Subject 1
Subject 2
Native
Spherical
Spherical
Surface-to-
Surface
Surface-to-
Surface
GLM
Demographics
mri_glmfit
cf. Talairach

## Slide 95
Borrowed from (Halgren et al., 1999)
Visualization

## Slide 96
Rosas et al., 2002
Kuperberg et al., 2003
Gold et al., 2005
Rauch et al., 2004
Salat et al., 2004
Fischl et al., 2000
Sailer et al., 2003

## Slide 97
Talk Outline
Cortical (surface-based) Analysis.
Volume Analysis.
New Features in 5.1.

## Slide 98
Volume Analysis: Automatic Individualized Segmentation
Surface-based coordinate system/registration appropriate for cortex but not for thalamus, ventricular system, basal ganglia, etc…
Anatomy is extremely variable – measuring the variance and accounting for it is critical (more in the individual subject talk)!

## Slide 99
FreeSurfer Version 5.1: New Features
Longitudinal Analysis (Martin Reuter).
Automated tractography with Tracula (Anastasia Yendiki).
Automated Hippocampal Subfield segmentation (Koen van Leemput).
New Architectonic Areas (entorhinal cortex, Jean Augustinack).
Open Source! (modified BSD/MIT license)

## Slide 100
The contribution of error is limited for outliers:
Unbiased Robust Registration*
Squared Error
Tukey's Biweight
*Reuter, Rosas and Fischl, 2010, NeuroImage

## Slide 101
New Areas: Entorhinal Cortex
Fischl et al., 2009, NeuroImage

## Slide 102
Comparing Coordinate Systems and Brodmann Areas
Cumulative histogram (red=surface, blue=nonlinear Talairach)
Ratio of surface accuracy to volume accuracy
Notes: Can use the ex vivo Brodmann delineations to assess the accuracy of a coordinate system. Of course being better than Talairach isn’t the strongest statement in the world….

## Slide 103
Longitudinal Analysis: Increased Reliability
Collaboration with Martin Reuter
14 subjects scanned twice, two weeks apart.