## Slide 1
Longitudinal FreeSurfer
by Martin Reuter
deep-mi.org

## Slide 2
1. Motivation​
2. Limitations and Biases
3. Unbiased Pipeline
4. Evaluations​
5. How to process your data?
Notes: At first, we will learn about the potential of working with longitudinal data, ​
We will discuss limitations and biases of longitudinal processing tools and designs, ​
and see how those limitations can be avoided in the unbiased processing pipeline implemented in both FastSurfer and FreeSurfer. ​
We will look at evaluations proving reduced bias and added value of this pipeline and finally, go over how to process your own longitudinal data​

## Slide 3
1. Motivation​

## Slide 4: What can we do with FreeSurfer?
Region segmentation and cortical surfaces
Region volumes and local cortical thickness
Study group differences (diseased vs. control)
4
Notes: So far, you have learned how to process brain images with FastSurfer and compute region segmentations and surfaces along the cortical sheet. ​
From those, you have computed statistics, such as region volumes and cortical thickness. ​
And as an example analysis, which you will learn about in the statistics session, you can find out if those estimates differ between groups, such as a diseased and control group. ​
​
Often, these analyses involve so-called cross-sectional data where each participant is scanned exactly once.​

## Slide 5: Longitudinal Data
Progression of Huntington’s Disease: 14 scans over 6 years
5
Notes: In contrast to cross-sectional data, longitudinal data consists of multiple scans for the same participants over time. ​
Here as an example , we see the progression of Huntington's disease in one individual over six years. ​
You can clearly see the changes: the ventricles growing and the corpus callosum bending upward and thinning. ​
And with longitudinal MRI data, we find that the majority of brain anatomy stays the same whereas we might observe changes locally. And with the analysis, we want use this observation to improve our estimates. ​
​

## Slide 6: Longitudinal Analysis
Improves estimates of morphological change over time
Detects smaller changes or requires fewer study participants
  Disease progression or atrophy rates
  Estimation of time to onset of symptoms
  Drug treatment assessment
6
Notes: Longitudinal analysis, when done right, can significantly improve our estimates of change in the brain's anatomy over time. ​
More specifically, the reduction in variability allows us to detect smaller changes or show some change with less participants – increasing the power of out analysis. ​
And these effects could be related to disease progression or atrophy rates, the estimation of time to onset of symptoms or the assessment of a drug treatment.​

## Slide 7: Example: Muscle Mass
Muscle Mass
Muscle Mass
Percent Change
young old
young old
young old
7
Notes: As a motivating example, let's say we wanted to study the development of muscle mass in a younger and an older population. ​
Given some cross-sectional data points, we compute the mean and the standard deviation for each group but statistical test tells us that the differences are not significant. ​
But if this was longitudinal data, we could build pairs and by doing this, we get a very exact and significant estimate of a 3% decline in muscle mass for the older population. ​
And the potential of discovering additional effects like this one in our data makes longitudinal studies so interesting!

## Slide 8
2. Limitations and Biases

## Slide 9
Method design limitations
  Only two time points
  Only same number of time points per participant
  Only subset of measures (WM/GM, only surfaces)
Over-Regularization
  Temporal smoothing
  Monotonicity assumptions
Processing Biases
  Interpolation asymmetry bias
  Asymmetric information transfer bias
Limitations and Biases
9
Notes: To begin with, methods designed can be restricting: They may allow only for two time points, require the same number of data points per participant or compute a subset of measurements. In contrast, with FreeSurfer and FastSurfer, we can do so much more.​
​
​
​

## Slide 10
Method design limitations
  Only two time points
  Only same number of time points per participant
  Only subset of measures (WM/GM, only surfaces)
Over-Regularization
  Temporal smoothing
  Monotonicity assumptions
Processing Biases
  Interpolation asymmetry bias
  Asymmetric information transfer bias
Limitations and Biases
10

## Slide 11
Method design limitations
  Only two time points
  Only same number of time points per participant
  Only subset of measures (WM/GM, only surfaces)
Over-Regularization
  Temporal smoothing
  Monotonicity assumptions
Processing Biases
  Interpolation asymmetry bias
  Asymmetric information transfer bias
Limitations and Biases
11
Notes: ​Another big problem arises from processing biases, for example the interpolation asymmetry bias​:
​
​

## Slide 12: Interpolation Asymmetry Bias
Pitfall: Mapping follow-up to baseline
  Baseline stays crisp, follow-up appears smoothed
  Often leads to overestimating change
t=1 (baseline)
t=2 (follow-up)
12
Notes: To learn about this bias, let's consider a study with two time points. Because we need to align both scans for our analysis, we might register the second timepoint onto the first. That's problematic because the first image is not mapped anywhere and stays crisp, whereas the second one get's mapped and resampled and looks smoothed.
​

## Slide 13
Original Image
13
Notes: To illustrate this effect, we consider just one scan. We take it and map it somewhere and map it back to its original orientation. In this process, we resample and interpolate twice.

## Slide 14
Twice Interpolated Image
14
Notes: We see how the brain tissue is smoothed and contrasts at tissue boundaries washed out compared to the crisp original.​

## Slide 15
Original Image
15
Notes: Now, if we fit surface models to both images, it appears that the white matter grows as the surface moves outward. But of course, this is the same image.

## Slide 16
Twice Interpolated Image
16

## Slide 17
MIRIAD dataset (65 participants)
Original (first session, first scan) vs. twice interpolated image
Interpolation Asymmetry Bias
17
Notes: Let's see how this affects a potential study. We take data from the MIRIAD dataset and map it back and forth resampling twice. We observe a huge decrease in GM volume and a huge increase in WM volume like in the images we just saw. But these changes are purely based on our processing, they are not real changes in the brain.​ And this bias has been discussed in the literature a few times.

## Slide 18
Limitations and Biases
Method design limitations
  Only two time points
  Only same number of time points per participant
  Only subset of measures (WM/GM, only surfaces)
Over-Regularization
  Temporal smoothing
  Monotonicity assumptions
Processing Biases
  Interpolation asymmetry bias
  Asymmetric information transfer bias
18
Notes: No another processing bias is the asymmetric information transfer bias which has not been discussed that much in the literature. This is going to be another example where images are processed differently or asymmetrically.

## Slide 19: Asymmetric Information Transfer Bias
19
t=3
t=5
19
t=4
t=2
t=1
Notes: To illustrate this bias, suppose, we have longitudinal data with 5 timepoints and want to analyze cortical thickness. ​

## Slide 20: Asymmetric Information Transfer Bias
Example:
Process baseline
20
t=3
t=5
20
t=2
t=1
t=4
Notes: So we obtain surfaces for our baseline. To get surfaces on the other timepoints, we map the baseline surfaces to the follow-ups and let them fine-tune a little longer to account for potential local changes. ​
While that may seem like a good idea, this strategy again treats the images differently, because you let the surfaces fine-tune longer on the follow-ups than we did on the baseline. ​
And this asymmetric processing might again compromise our study results!
Also asymmetry because of anatomy of baseline!

## Slide 21: Asymmetric Information Transfer Bias
Example:
Process baseline
Transfer results from baseline to follow-up and fine-tune surfaces there
Can introduce bias!
21
t=3
t=5
21
t=2
t=1
t=4
Notes: So we obtain surfaces for our baseline. To get surfaces on the other timepoints, we map the baseline surfaces to the follow-ups and let them fine-tune a little longer to account for potential local changes. ​
While that may seem like a good idea, this strategy again treats the images differently, because you let the surfaces fine-tune longer on the follow-ups than we did on the baseline. ​
And this asymmetric processing might again compromise our study results!
Also asymmetry because of anatomy of baseline!

## Slide 22
3. Unbiased Pipeline

## Slide 23
t=3
t=5
23
t=2
t=1
t=3
t=5
23
t=4
t=2
t=1
How can we avoid the pitfalls?
biased
unbiased
23
t=4
Notes: In contrast to the biased strategy which treats images differently, we aim for an unbiased one that treats all time points the same.​

## Slide 24
We need:
  a) Unbiased and symmetric registration
  b) Approach to reduce influence of outliers and changes
In the presence of outliers and changes:
  Noise
  Gradient non-linearities
  Movement: jaw, tongue, neck, eye, scalp ...
  Cropping
  Longitudinal changes (atrophy)
Robust Registration
Reuter et al. (2010a)
24
Notes: One part of this pipeline a registration mechanism bringing different images into alignment. This registration needs to be unbiased and symmetric and should reduce the influence of outliers and changes that might distort the registration process. And this needs to be accomplished in the presence of noise, gradient-nonlinearities, various modes of movement, different cropping planes and, of course, longitudinal changes.​

## Slide 25
We need:
  a) Unbiased and symmetric registration
  b) Approach to reduce influence of outliers and changes
In the presence of outliers and changes:
  Noise
  Gradient non-linearities
  Movement: jaw, tongue, neck, eye, scalp ...
  Cropping
  Longitudinal changes (atrophy)
Robust Registration
Reuter et al. (2010a)
25

## Slide 26: a) Unbiased and Symmetric Registration
transform M
Moving / Source
Fixed / Reference / Target / Destination
26
Notes: So, usually, registration involves directionality, A moving or source images gets registered onto a fixed and reference image. And this returns some mapping M describing the transform.

## Slide 27: a) Unbiased and Symmetric Registration
transform M
transform M'
Moving / Source
Fixed / Reference / Target / Destination
Generally: M' ≠ M-1
⇒ Bias
27
Notes: Now, if you were to register in the other direction, you would get some other transformation M' which is generally not equal to M inverse which implies a bias. In other words, it matters which direction you choose and its not symmetric. ​
​
​
​
​

## Slide 28: a) Unbiased and Symmetric Registration
Unbiased mid-space (symmetric and inverse-consistent)​
No directionality between images (source: both images, target: mid-space)​
We find the symmetric mapping iteratively ​
Reuter et al. (2010a)
28
Notes: A way to make it symmetric is to map both images into an unbiased mid space.
And this solution is also inverse-consistent and involves no directionality anymore.
The mid-space is initially unknown and determined iteratively by the registration's cost function.​
​
​
​

## Slide 29: a) Unbiased and Symmetric Registration
Inverse consistency of different methods on original (orig), intensity normalized (T1) and skull stripped (norm) images.
LS and Robust:
nearly perfect symmetry (worst case RMS < 0.02)
Other methods:
several alignments with RMS errors > 0.1
29
Notes: This evaluation compares the symmetry of different registration algorithms.
We take two images, obtain a mapping from A to B and one from B to A.
For different variants of FLIRT and SPM, the blue and green error bars are​ large.
However, for the robust registration, they are very low, indicating a very high degree of symmetry.​

## Slide 30: Robust Registration
Reuter et al. (2010a)
We need:
  a) Unbiased and symmetric registration
  b) Approach to reduce influence of outliers and changes
In the presence of outliers and changes:
  Noise
  Gradient non-linearities
  Movement: jaw, tongue, neck, eye, scalp ...
  Cropping
  Longitudinal changes (atrophy)
30
Notes: Now that we have the unbiased and symmetric registration, we move on to reducing the influence of outliers and changes.

## Slide 31: b) Reducing the influence of outliers
Tumor data with significant intensity differences in the brain,
registered to first time point (left).
31
Notes: Let's consider this time series where a brain tumor develops over time. Because the tumor is so large, the intensity variation in the tumor region may distort the agreement of the brains overall. So we are looking for a mechanism that can register the brains accurately while handling outliers in robust way.​

## Slide 32: b) Reducing the influence of outliers
Square
Tukey's Biweight
Nestares and Heeger (2000)
32
Notes: One way to that is to replace the cost function in the registration. Usually the squared error is used where outliers are assigned quadratically growing importance. However, by replacing this with the so-called Tukey's biweight function, the role of outliers is limited and the mechanism will ignore large-enough outliers instead of over-fixating on them at the cost of the agreement in the rest of the image.

## Slide 33: b) Reducing the influence of outliers
Tumor data with significant intensity differences in the brain,
registered to first time point (left).
33
Notes: Going back to our tumor time series, we see that this actually works. In the bottom row, we see the registered images with an overlay indicating the local importance to the registration, going from yellow meaning its essentially ignored​
To transparent meaning very important. And we observe that both tumor regions on the left and right and also the expanding ventricles were basically ignored such that the rest of the brain can be registered accurately.​

## Slide 34: b) Reducing the influence of outliers
Registered Source FLIRT
Registered Source Robust
34
Notes: So, here we look at images with very different neck orientations. And while the FSL registration FLIRT cannot accurately register these brains considering the neck outlier region, the robust registration approach on the right obtains a very accurate registration.

## Slide 35
Target
Target
35
b) Reducing the influence of outliers
Notes: In this comparison with the FSL registration FLIRT, we observe a misregistration for FLIRT as indicated by the arrow, while the robust registration approach accurately registers the two brains despite significant movement of the neck.

## Slide 36: Robust Registration
We need:
  a) Unbiased and symmetric registration ✓
  b) Approach to reduce influence of outliers and changes ✓
In the presence of outliers and changes:
  Noise
  Gradient non-linearities
  Movement: jaw, tongue, neck, eye, scalp ...
  Cropping
  Longitudinal changes (atrophy)
Reuter et al. (2010a)
36
Notes: Now, with the unbiased and symmetric registration and the robust approach towards outliers, our robust registration is established.

## Slide 37: Robust Within-Person Template
Iterative Template Creation:
1. Compute template
2. Map images to iteration template
Reuter et al. (2010b), Reuter and Fischl (2011), Reuter et al. (2012)​
37
t=3
t=5
37
t=4
t=2
t=1
Notes: ​Now we know about robust registration and the mid-space. ​
And we could use this to conduct a longitudinal analysis with two timepoints. ​
But our data generally has more than two timepoints. ​
To handle this, we can extend the mid-space idea to any number of brains or time points. ​
But here, we change the terminology and say we obtain a within-person template which is essentially a mid-space of all time points. ​
To find it given some number of brains, we use the same strategy that already worked for two brains: we obtain a median template image, register the time points there, obtain the next template image, map the images there and so on until the final template image is found. ​

## Slide 38: Robust Registration and Template
mri_robust_register and mri_robust_template
implemented in FreeSurfer
also in Python Tool: `pip install neuroreg`
can be used independently of the longitudinal pipeline
mri_robust_register for pair-wise registration (optimally within-person, within-modality)
38
Notes: Both the robust registration and the robust template are functions in FreeSurfer and they can be used also independently of the longitudinal pipeline. ​
You would use "mri_robust_register" for a registration of two images into a common mid-space. ​
Here, we can output the images in the mid-space and also visualize the outlier-weights as we saw earlier. And this is a very general registration function, s you could also use this for T2 images.​
In contrast, if you have more than two images, you would use the function "mri_robust_template".​
​

## Slide 39: Longitudinal FastSurfer / FreeSurfer
Workflow
Create the within-person template
Reuter et al. (2010b), Reuter and Fischl (2011), Reuter et al. (2012)​
39
t=3
t=5
39
t=4
t=2
t=1
Notes: Now, how does this all connect to the longitudinal pipeline, the segmentations and the surfaces? ​

## Slide 40: Longitudinal FastSurfer / FreeSurfer
Workflow
Create the within-person template
Reuter et al. (2010b), Reuter and Fischl (2011), Reuter et al. (2012)​
40
t=3
t=5
40
t=4
t=2
t=1
Notes: This final pipeline looks as follows: First, we generate the within-person template given N timepoints​

## Slide 41: Longitudinal FastSurfer / FreeSurfer
Workflow
Create the within-person template
Generate segmentations and surfaces for the template
Reuter et al. (2010b), Reuter and Fischl (2011), Reuter et al. (2012)​
41
t=3
t=5
41
t=4
t=2
t=1
Notes: Second, we generate segmentations and surfaces with FreeSurfer or FastSurfer for the within-person template.​

## Slide 42: Longitudinal FastSurfer / FreeSurfer
Workflow
Create the within-person template
Generate segmentations and surfaces for the template
Initialize the timepoint surfaces with template surfaces and finetune
Reuter et al. (2010b), Reuter and Fischl (2011), Reuter et al. (2012)​
42
t=3
t=5
42
t=4
t=2
t=1
Notes: And third, we initialize the time-point-specific surfaces with the template surface and let it fine-tune longer to adjust to a potentially time-point-specific anatomy. ​
Earlier, we talked about the asymmetric information transfer bias, where images were handled differently and some surfaces fine-tuned longer than others. ​
With this pipeline we avoid all of that. All of the processing takes place in the symmetric template space and surfaces can fine-tune equally long on all time points.​

## Slide 43: Asymmetric Information Transfer Bias
Biased information transfer: [BASE1] and [BASE2].
Longitudinal FreeSurfer [FS-LONG] [FS-LONG-rev] shows no bias.
Cortical
Test-Retest (115 study participants, 2 scans, same session)
Subcortical
Reuter et al. (2010b), Reuter and Fischl (2011), Reuter et al. (2012)​
43
Notes: This evaluation quantifies the asymmetric information transfer bias between different methods.​
We are working with data from 115 participants who were scanned twice in one session. Hence, we can assume no anatomical changes.
​And with the two base approaches, we follow the biased approach from earlier, we run FreeSurfer, map the results to the second timepoint and let it fine-tune which. In base 2, we reverse the role of the time points and then we evaluate both orders with the new longitudinal pipeline.
And with the biased approach, we find significant volume changes when there should not be any and we also see a reversal of effects depending on which direction wie transfer the data in. ​
However, in contrast, with the longitudinal pipeline, this effect is gone underlining the added value of this pipeline.

## Slide 44
Method design limitations
  Only two time points ✓
  Only same number of time points per participant ✓
  Only subset of measures (WM/GM, only surfaces) ✓
Over-Regularization
  Temporal smoothing ✓
  Monotonicity assumptions ✓
Processing Biases
  Interpolation asymmetry bias ✓
  Asymmetric information transfer bias ✓
Limitations and Biases
44
Notes: In summary, this pipeline overcomes a lot of the limitations and biases of other pipelines and designs.It does not have these design limitations, it does apply temporal smoothing or monotonicity assumptions and it was specifically designed to avoid these two processing biases.
​
​
​
​

## Slide 45
4. Evaluations​

## Slide 46: 1) Region Volume Reliability
Longitudinal FreeSurfer [LONG] significantly improves reliability
115 study participants, MEMPRAGE, 2 scans, same session
Subcortical
Cortical
Reuter et al. (2012)
Variance
Variance
46
Notes: In this evaluation, we look at region reliability for the independent processing and the longitudinal FreeSurfer stream. ​
We take the same dataset as before with the same session data, where we don’t expect any volume change at al. ​
However, for the independent processing -- the green bars -- we observe a high degree of variance where we don't expect any and this effect is much reduced when using the longitudinal stream -- the yellow bars -- giving us more reliable results. ​
​

## Slide 47: 2) Sample Sizes
Sample Size Reduction when using longitudinal FreeSurfer [LONG]
(based on test-retest 14 study participants, 2 weeks)
Reuter et al. (2012)
Percent Participants needed (LONG vs. CROSS)
47
Notes: This increased reliability of the longitudinal stream translates into increased power in our statistical testing. This graph shows the percent of participants needed to show the same effects as the independent processing. ​
These numbers lie between 20 and 60 percent which is a huge saving in resources -- Illustrating that studies can be done with a fraction of the participants when using the right tools. Or alternatively, given a number of participants, you could find smaller effects.​

## Slide 48: 3) Cortical Thickness Reliability
FreeSurfer
FreeSurfer-long
OASIS, N=20, Abs(diff): 0 mm ➔ > 0.1 mm
48
Notes: Now, the FastSurfer longitudinal stream increases this reliability even more.

## Slide 49: 3) Cortical Thickness Reliability
FreeSurfer
FreeSurfer-long
FastSurfer-long
FastSurfer
OASIS, N=20, Abs(diff): 0 mm ➔ > 0.1 mm
49
Notes: Now, the FastSurfer longitudinal stream increases this reliability even more.

## Slide 50
FreeSurfer
FreeSurfer-long
Dementia Oasis 2, N=271, p=0.05 ➔ p=0.00001
4) Group Analysis
50
Notes: And the FastSurfer longitudinal stream shows even more significant regions – showing the highest capability to separate dementia and control participants.​
​

## Slide 51
FreeSurfer
FreeSurfer-long
FastSurfer-long
FastSurfer
Dementia Oasis 2, N=271, p=0.05 ➔ p=0.00001
4) Group Analysis
51
Notes: And the FastSurfer longitudinal stream shows even more significant regions – showing the highest capability to separate dementia and control participants.​
​

## Slide 52
Longitudinal FreeSurfer [LONG] shows higher precision and better
discrimination power between groups (specificity and sensitivity).
Independent Processing
Longitudinal Processing
5) Huntington’s Disease Analysis
Reuter et al. (2012)
52
Notes: And with this evaluation we show the application to actual pathology: Huntington's disease. ​
We have four groups: a control group, people more than 12 years before estimated time of symptom onset, people that are closer to onset, and people with Huntington's disease.​
And based on three visits, we can calculate changes in region volumes per year.​
For the independent processing on the left, we get pretty noisy results with large error bars but they suggest a clear volume decay.
​
However, when using the longitudinal stream, we observe that the atrophy rate usually is accelerating and error bars are smaller. ​
We can find significant differences between neighboring groups which we couldn't for the independent processing, for example between control and far from onset for the caudate and putamen regions.​
These regions are involved in early HD and with the longitudinal stream, we can detect these group differences even 12 years before symptom onset on a small dataset.​
​
​

## Slide 53
Rate of Atrophy
Baseline Vol. (normalized)
5) Huntington’s Disease Analysis
Reuter et al. (2012)
Putamen Atrophy Rate is significantly different between CN and
PHDfar, but baseline volume is not.
53
Notes: And its also interesting to look at cross-sectional volumes at baseline (on the right). But although there is also a clear direction, we we can not distinguish neighboring groups – not like we can with the longitudinal processing (on the left) underlining again the value of this pipeline for finding significant effects.

## Slide 54
5. How to process your data?

## Slide 55
Unbiased
Reduces Variability
Common space for:
  - TIV estimation
  - Skullstrip
  - Affine Talairach Registration
Basis for:
  - Intensity Normalization
  - Non-linear Registration
  - Surfaces / Parcellation
Robust Template for Initialization

## Slide 56: FreeSurfer Commands: recon-all
recon-all –subjid <tp#name> -i <path_to_tp#_t1> -all
For each time point # create cross sectional run, e.g. bert1
56
1. CROSS independent processing (for each time point)

## Slide 57: FreeSurfer Commands: recon-all
recon-all –subjid <tp#name> -i <path_to_tp#_t1> -all
57
1. CROSS independent processing (for each time point)
2. BASE create template (one per participant)
recon-all –base <template_name> \
Name for the template, e.g., bert_template

## Slide 58: FreeSurfer Commands: recon-all
recon-all –subjid <tp#name> -i <path_to_tp#_t1> -all
Specify all time points, bert1 …
58
1. CROSS independent processing (for each time point)
2. BASE create template (one per participant)
recon-all –base <template_name> \
-tp <tp1name> -tp <tp2name> … -all

## Slide 59: FreeSurfer Commands: recon-all
recon-all –subjid <tp#name> -i <path_to_tp#_t1> -all
E.g. –long bert1 bert_template
59
1. CROSS independent processing (for each time point)
2. BASE create template (one per participant)
recon-all –base <template_name> \
-tp <tp1name> -tp <tp2name> … -all
3. LONG longitudinal processing (for each time point)
recon-all –long <tp#name> <template_name> -all

## Slide 60: Output in $subjects_dir
60
Contains all CROSS, BASE and LONG data
bert1
bert2
bert3
bert_template
bert1.long.bert_template
bert2.long.bert_template
bert3.long.bert_template
ernie1
…
Final results to use in statistics!

## Slide 61
Participants with only one time point
Should be included but need to be processed the same to avoid bias
Longitudinal statistics: We recommend linear mixed effects models
our FS LME R toolbox (github.com/Deep-MI/fslmer)
our FS LME Matlab package (github.com/NeuroStats/lme)
Manual Edits:
Order: CROSS, BASE, then LONG should be fixed automatically
Often it is enough to just edit BASE
http://freesurfer.net/fswiki/LongitudinalEdits
Longitudinal Analysis
61
recon-all –subjid bert_tp1 -i <path_to_tp1_t1> -all
recon-all –base bert_template -tp bert_tp1 -all
recon-all –long bert_tp1 bert_template -all
Notes: One additional remark concerns participants with only one timepoint. ​
This might be someone who dropped out of the study or just started. ​
These can add value to your study but obviously not in a longitudinal sense. ​
To avoid bias, you'll want to process their data analogously to the other data and you can. ​
Internally their data will be mapped to a pseudo-within-person template and we can be sure that this data will be resampled similarly to the other participants who have more time points. ​
Now that you have processed your data, you'll want to reach some conclusions by means of statistical analysis. ​
For this, we recommend linear mixed effects models and for that you're invited to use our tools but you will learn about those in session tomorrow.​

## Slide 62
Process CROSS, BASE, LONG
Statistics
  Atrophy rates per participant
  Group analysis (compare rates)
Vocabulary:
Temporal Average
Rate of Change
Percent Change (w.r.t. time 1)
Symmetrized Percent Change (w.r.t. temp. avg.)
Longitudinal Tutorial

## Slide 63
Influence images directly and cannot be easily removed!
Different scanner hardware (head coil, pillow?)
Different scanner software (shimming algorithm)
Scanner drift and calibration
Different hydration levels (season, time of day)
Different motion levels across groups
Sources of Bias during Acquisition
63
Notes: One additional remark concerns participants with only one timepoint. ​
This might be someone who dropped out of the study or just started. ​
These can add value to your study but obviously not in a longitudinal sense. ​
To avoid bias, you'll want to process their data analogously to the other data and you can. ​
Internally their data will be mapped to a pseudo-within-person template and we can be sure that this data will be resampled similarly to the other participants who have more time points. ​
Now that you have processed your data, you'll want to reach some conclusions by means of statistical analysis. ​
For this, we recommend linear mixed effects models and for that you're invited to use our tools but you will learn about those in session tomorrow.​

## Slide 64
14 participants, 12h dehydration (over night)
Hydration Levels
Biller et al. (2015)
64
Notes: Here, the influence of hydration levels was examined. In this first row, we see how cortical thickness estimates change when participants are dehydrated suggesting cortical thinning with respect to a baseline.​
​

## Slide 65
14 participants, 12h dehydration (over night)
rehydration 1L/h
Hydration Levels
Biller et al. (2015)
65
Notes: In contrast, when the same participants rehydrate and are scanned again, the cortical thickness analysis suggests that thickening with respect to the dehydrated state in the first row. Of course, these scans are taken in close succession and there are no cortical changes, its simply caused by differences in hydration levels. ​

## Slide 66
12 volunteers
5 motion types:
  2 Still
  Nod
  Shake
  Free
Duration:
  5-15 s/min
Effect:
roughly 0.7-1% volume loss per 1mm/min increase in motion
Motion Biases Gray Matter Estimates
Reuter et al. (2014)
66
Notes: Lastly, this evaluation examines the relationship between motion and cortical gray matter volume suggesting that cortical grey matter volume estimates are lower when participants move more in the scanner. And this is related to the interpolation smoothing we saw in the beginning.​

## Slide 67
12 volunteers
5 motion types:
  2 Still
  Nod
  Shake
  Free
Duration:
  5-15 s/min
Effect:
roughly 0.7-1% volume loss per 1mm/min increase in motion
Motion Biases Gray Matter Estimates
Reuter et al. (2014)
67
Notes: And here we have similar results not for FreeSurfer but another processing suite – SPM, indicating the same trend. ​
So these are additional biases to be aware of when conducting your study. ​
In summary, in this session you have learned a lot about biases and pitfalls in longitudinal data processing, ​
you have learned how to remove asymmetry and bias from processing, ​
how this is implemented in FastSurfer and FreeSurfer, ​
we looked at evaluations showing that biases are at least significantly reduced and that the longitudinal stream increases the reliability for volume and surface estimates, ​
That this reliability can significantly reduce the number of participants need to show effects, ​
increases the reliability in a group study and HD analysis. ​
And finally, you have learned how to actually process you own data with the longitudinal streams of FastSurfer and FreeSurfer.​
And now, we have some additional time for questions. ​

## Slide 68
Motion in Statistical Analyses
68
Clemens Pollak et al. (2023) analyzed head motion in the Rhineland Study with a camera system
Without a camera system:
  Use fMRI motion as proxy for T1w motion (highly correlated)
  Motion tool: fMRI motion → motion score
  Use motion score in your analysis
https://github.com/Deep-MI/head-motion-tools
Notes: ​

## Slide 69
Biller, Reuter, Patenaude, Homola, Breuer, Bendszus, and Bartsch (2015): "Responses of the Human Brain to Mild Dehydration and Rehydration Explored In Vivo by 1H-MR Imaging and Spectroscopy", American Journal of Neuroradiology​
Nestares and Heeger (2000): "Robust multiresolution alignment of MRI brain volumes", Magnetic Resonance in Medicine​
Pollak, Kügler, Breteler, and Reuter (2023): "Quantifying MR head motion in the Rhineland Study ​ – A robust method for population cohorts", NeuroImage​
Reuter, Rosas, and Fischl (2010a): "Highly accurate inverse consistent registration: a robust approach", NeuroImage​
Reuter, Rosas, and Fischl (2010b) "Unbiased robust template estimation for longitudinal analysis in FreeSurfer", Proceedings of the 16th Annual Meeting of the Organization for Human Brain Mapping​
Reuter and Fischl (2011): "Avoiding asymmetry-induced bias in longitudinal image processing", NeuroImage​
Reuter, Schmansky, Rosas, and Fischl (2012): "Within-subject template estimation for unbiased longitudinal image analysis", NeuroImage​
Reuter, Tisdall, Qureshi, Buckner, van der Kouwe, and Fischl (2014): "Head Motion during MRI Acquisition Reduces Gray Matter Volume and Thickness Estimates", NeuroImage ​
References
69