## Slide 1
1
Anatomical Analysis with FreeSurfer surfer.nmr.mgh.harvard.edu
Notes: Look at reconstruction steps in depth
Serves to familiarize with reconstruction steps for individual subject.
Important to be familiar with steps for intervention, QA, troubleshooting errors you may encounter.
1

## Slide 2
2
Individual Processing Stream Overview
Skull Stripping
Gyral Labeling
Intensity Normalization
Surface Extraction
Surface Atlas
Registration
Subcortical
Mass
T1 Weighted
Input
Stats
Volumetric Labeling
Notes: 2
-T1-weighted (wm brighter than gm)
-If higher res, gets downsampled (1mm isotropic)
-Can’t go lower than 1.5mm^3

## Slide 3
3
Input: T1 Weighted Image
T1 Contrast: white matter brighter than gray matter
~1mm3 (no more than 1.5mm)
Higher resolution may be worse!
Full Brain
Usually one acquisition is ok
MPRAGE (ME-MP-RAGE) or SPGR
1.5T or 3T
7T might have problems
Subject age > 5 years old
Brain has no major problems (ie, tumors, parts missing)
Non-human primates possible
More MRI Pulse Sequence Parameter Details:
http://www.nmr.mgh.harvard.edu/~andre
http://adni.loni.usc.edu/methods/documents/mri-protocols
Notes: 3

## Slide 4
4
Fully Automated Reconstruction
recon-all –i file.dcm –subject bert –all
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
4

## Slide 5
5
Fully Automated Reconstruction
recon-all
–i file.dcm
–subject bert
–all
file.dcm is a single DICOM file from the T1 MRI series.
If you have more than one T1, then use:
–i file1.dcm –i file2.dcm
You can use NIFTI as well with
–i file.nii
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
5

## Slide 6
Finding file.dcm is sometimes the hardest part …
DICOM files as they might look when they come off the scanner (thousands of them):
MR.1.3.12.2.1107.5.2.43.67026.201711091646082874533087 MR.1.3.12.2.1107.5.2.43.67026.2017110917191282573911820
MR.1.3.12.2.1107.5.2.43.67026.2017110916460829881533294 MR.1.3.12.2.1107.5.2.43.67026.201711091719169256012022
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830223533295 MR.1.3.12.2.1107.5.2.43.67026.2017110917191928591512224
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830251133297 MR.1.3.12.2.1107.5.2.43.67026.2017110917192251641412426
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830839833301 MR.1.3.12.2.1107.5.2.43.67026.2017110917192596977912636
MR.1.3.12.2.1107.5.2.43.67026.201711091646083115933088 MR.1.3.12.2.1107.5.2.43.67026.201711091719291307712830
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831838233312 MR.1.3.12.2.1107.5.2.43.67026.2017110917193220348113032
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831854033313 MR.1.3.12.2.1107.5.2.43.67026.2017110917193543755013234
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831890833314 MR.1.3.12.2.1107.5.2.43.67026.2017110917193866363913436
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831999633315 MR.1.3.12.2.1107.5.2.43.67026.2017110917194188432513634
MR.1.3.12.2.1107.5.2.43.67026.2017110916460832005833316 MR.1.3.12.2.1107.5.2.43.67026.2017110917194189797813639
MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
You only need one, but which one is the anatomical?
recon-all
–i file.dcm
–subject bert
–all
6
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
6

## Slide 7
Use dcmunpack, eg,
dcmunpack –src /path/to/dicoms
DICOM files as they might look when they come off the scanner (thousands of them)
MR.1.3.12.2.1107.5.2.43.67026.201711091646082874533087 MR.1.3.12.2.1107.5.2.43.67026.2017110917191282573911820
MR.1.3.12.2.1107.5.2.43.67026.2017110916460829881533294 MR.1.3.12.2.1107.5.2.43.67026.201711091719169256012022
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830223533295 MR.1.3.12.2.1107.5.2.43.67026.2017110917191928591512224
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830251133297 MR.1.3.12.2.1107.5.2.43.67026.2017110917192251641412426
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830839833301 MR.1.3.12.2.1107.5.2.43.67026.2017110917192596977912636
MR.1.3.12.2.1107.5.2.43.67026.201711091646083115933088 MR.1.3.12.2.1107.5.2.43.67026.201711091719291307712830
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831838233312 MR.1.3.12.2.1107.5.2.43.67026.2017110917193220348113032
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831854033313 MR.1.3.12.2.1107.5.2.43.67026.2017110917193543755013234
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831890833314 MR.1.3.12.2.1107.5.2.43.67026.2017110917193866363913436
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831999633315 MR.1.3.12.2.1107.5.2.43.67026.2017110917194188432513634
MR.1.3.12.2.1107.5.2.43.67026.2017110916460832005833316 MR.1.3.12.2.1107.5.2.43.67026.2017110917194189797813639
MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
Example output of dcmunpack
1 Localizer 3 40 15 1.171875\1.171875 MR.1.3.12.2.1107.5.2.43.67026.2017110915514228348456487
2 AAHScout 1.37 3.15 8 1.625\1.625 ROW 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520120516357516
3 AAHScout_MPR_sag 1.37 3.15 8 1.60000002384\1.60000002384 unknown 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520123687057660
4 AAHScout_MPR_cor 1.37 3.15 8 1.60000002384\1.60000002384 unknown 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520123821357667
5 AAHScout_MPR_tra 1.37 3.15 8 1.60000002384\1.60000002384 unknown 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520123877057670
6 Localizer_aligned 3 104 15 1.171875\1.171875 ROW 260 MR.1.3.12.2.1107.5.2.43.67026.2017110915522716700857682
7 T1w_setter 4.6 9.9 2 unknown ROW 5210 MR.1.3.12.2.1107.5.2.43.67026.201711091554416141157795
8 T1w_setter 4.6 9.9 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916004795330874762
9 T1w_MPR_vNav_4e 3.55 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916021229775680242
10 T1w_MPR_vNav_4e 7.27 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916020532284777889
11 T1w_MPR_vNav_4e 3.55 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916021487561780704
12 T1w_MPR_vNav_4eRMS 1.69 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916021957542181407
13 T1w_MPR_vNav_4eRMS 1.69 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
MP-RAGE T1 Protocol
This will be different for everyone
You will have to know what this name is
Finding file.dcm is sometimes the hardest part …
7
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
7

## Slide 8
Use dcmunpack, eg,
dcmunpack –src /path/to/dicoms
DICOM files as they might look when they come off the scanner (thousands of them)
MR.1.3.12.2.1107.5.2.43.67026.201711091646082874533087 MR.1.3.12.2.1107.5.2.43.67026.2017110917191282573911820
MR.1.3.12.2.1107.5.2.43.67026.2017110916460829881533294 MR.1.3.12.2.1107.5.2.43.67026.201711091719169256012022
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830223533295 MR.1.3.12.2.1107.5.2.43.67026.2017110917191928591512224
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830251133297 MR.1.3.12.2.1107.5.2.43.67026.2017110917192251641412426
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830839833301 MR.1.3.12.2.1107.5.2.43.67026.2017110917192596977912636
MR.1.3.12.2.1107.5.2.43.67026.201711091646083115933088 MR.1.3.12.2.1107.5.2.43.67026.201711091719291307712830
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831838233312 MR.1.3.12.2.1107.5.2.43.67026.2017110917193220348113032
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831854033313 MR.1.3.12.2.1107.5.2.43.67026.2017110917193543755013234
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831890833314 MR.1.3.12.2.1107.5.2.43.67026.2017110917193866363913436
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831999633315 MR.1.3.12.2.1107.5.2.43.67026.2017110917194188432513634
MR.1.3.12.2.1107.5.2.43.67026.2017110916460832005833316 MR.1.3.12.2.1107.5.2.43.67026.2017110917194189797813639
MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
Example output of dcmunpack
1 Localizer 3 40 15 1.171875\1.171875 MR.1.3.12.2.1107.5.2.43.67026.2017110915514228348456487
2 AAHScout 1.37 3.15 8 1.625\1.625 ROW 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520120516357516
3 AAHScout_MPR_sag 1.37 3.15 8 1.60000002384\1.60000002384 unknown 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520123687057660
4 AAHScout_MPR_cor 1.37 3.15 8 1.60000002384\1.60000002384 unknown 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520123821357667
5 AAHScout_MPR_tra 1.37 3.15 8 1.60000002384\1.60000002384 unknown 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520123877057670
6 Localizer_aligned 3 104 15 1.171875\1.171875 ROW 260 MR.1.3.12.2.1107.5.2.43.67026.2017110915522716700857682
7 T1w_setter 4.6 9.9 2 unknown ROW 5210 MR.1.3.12.2.1107.5.2.43.67026.201711091554416141157795
8 T1w_setter 4.6 9.9 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916004795330874762
9 T1w_MPR_vNav_4e 3.55 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916021229775680242
10 T1w_MPR_vNav_4e 7.27 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916020532284777889
11 T1w_MPR_vNav_4e 3.55 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916021487561780704
12 T1w_MPR_vNav_4eRMS 1.69 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916021957542181407
13 T1w_MPR_vNav_4eRMS 1.69 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
A single DICOM file that belongs to the MPRAGE series (there might be several hundred; you only need one).
Finding file.dcm is sometimes the hardest part …
8
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
8

## Slide 9
recon-all –i MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
–subject bert –all
Use dcmunpack, eg,
dcmunpack –src /path/to/dicoms
DICOM files as they might look when they come off the scanner (thousands of them)
MR.1.3.12.2.1107.5.2.43.67026.201711091646082874533087 MR.1.3.12.2.1107.5.2.43.67026.2017110917191282573911820
MR.1.3.12.2.1107.5.2.43.67026.2017110916460829881533294 MR.1.3.12.2.1107.5.2.43.67026.201711091719169256012022
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830223533295 MR.1.3.12.2.1107.5.2.43.67026.2017110917191928591512224
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830251133297 MR.1.3.12.2.1107.5.2.43.67026.2017110917192251641412426
MR.1.3.12.2.1107.5.2.43.67026.2017110916460830839833301 MR.1.3.12.2.1107.5.2.43.67026.2017110917192596977912636
MR.1.3.12.2.1107.5.2.43.67026.201711091646083115933088 MR.1.3.12.2.1107.5.2.43.67026.201711091719291307712830
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831838233312 MR.1.3.12.2.1107.5.2.43.67026.2017110917193220348113032
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831854033313 MR.1.3.12.2.1107.5.2.43.67026.2017110917193543755013234
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831890833314 MR.1.3.12.2.1107.5.2.43.67026.2017110917193866363913436
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831999633315 MR.1.3.12.2.1107.5.2.43.67026.2017110917194188432513634
MR.1.3.12.2.1107.5.2.43.67026.2017110916460832005833316 MR.1.3.12.2.1107.5.2.43.67026.2017110917194189797813639
MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
Example output of dcmunpack
1 Localizer 3 40 15 1.171875\1.171875 MR.1.3.12.2.1107.5.2.43.67026.2017110915514228348456487
2 AAHScout 1.37 3.15 8 1.625\1.625 ROW 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520120516357516
3 AAHScout_MPR_sag 1.37 3.15 8 1.60000002384\1.60000002384 unknown 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520123687057660
4 AAHScout_MPR_cor 1.37 3.15 8 1.60000002384\1.60000002384 unknown 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520123821357667
5 AAHScout_MPR_tra 1.37 3.15 8 1.60000002384\1.60000002384 unknown 540 MR.1.3.12.2.1107.5.2.43.67026.2017110915520123877057670
6 Localizer_aligned 3 104 15 1.171875\1.171875 ROW 260 MR.1.3.12.2.1107.5.2.43.67026.2017110915522716700857682
7 T1w_setter 4.6 9.9 2 unknown ROW 5210 MR.1.3.12.2.1107.5.2.43.67026.201711091554416141157795
8 T1w_setter 4.6 9.9 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916004795330874762
9 T1w_MPR_vNav_4e 3.55 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916021229775680242
10 T1w_MPR_vNav_4e 7.27 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916020532284777889
11 T1w_MPR_vNav_4e 3.55 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916021487561780704
12 T1w_MPR_vNav_4eRMS 1.69 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916021957542181407
13 T1w_MPR_vNav_4eRMS 1.69 2530 7 unknown ROW 650 MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
https://surfer.nmr.mgh.harvard.edu/fswiki/FsTutorial/Practice
Finding file.dcm is sometimes the hardest part …
9
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
9

## Slide 10
10
Fully Automated Reconstruction
recon-all
–i file.dcm
–subject bert
–all
“bert” is the “name” of the subject
Creates a folder in $SUBJECTS_DIR
All output goes in this folder (~400MB)
Other subjects in $SUBJECTS_DIR
bert
$SUBJECTS_DIR
ernie
fsaverage …
setenv SUBJECTS_DIR /path/to/space
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
10

## Slide 11
11
Fully Automated Reconstruction
recon-all
–i file.dcm
–subject bert
–all
-all means to do everything!
Can take 10-13 hours (next version about half that time)
Later, we will show you how to run subsets of the processing stream to make it faster when correcting errors.
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
11

## Slide 12
12
Upon Completion…
$SUBJECTS_DIR/bert
scripts mri surf label stats
recon-all –i file.dcm –subject bert –all
~400MB
Notes: 12
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 13
13
Upon Completion…
bert
scripts mri surf label stats
recon-all.log
recon-all.done
Just because it finishes “without error” does not mean that everything is ok!
Send us recon-all.log when you have problems! freesurfer@nmr.mgh.harvard.edu
Notes: 13
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 14
14
Upon Completion…
bert
scripts mri surf label stats
orig.mgz
T1.mgz
brainmask.mgz
filled.mgz
aseg.mgz
mgz = “compressed mgh” format (like nifti) unique to FreeSurfer
rawavg.mgz
others: nu.mgz, norm.mgz, wmparc.mgz, aparc+aseg.mgz, ribbon.mgz
Notes: 14
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 15
15
Upon Completion…
bert
scripts mri surf label stats
orig.mgz
T1.mgz
brainmask.mgz
rawavg.mgz
Native Anatomical Space
eg, 1x1x1.2mm3 , 256x256x128
“Conformed” Anatomical Space
1x1x1mm3 , 256x256x256
filled.mgz
aseg.mgz
Notes: 15
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 16
16
Upon Completion…
bert
scripts mri surf label stats
lh.orig
lh.white
lh.pial
lh.inflated
lh.sphere.reg
rh.orig
rh.white
rh.pial
rh.inflated
rh.sphere.reg
lh.thickness and rh.thickness, ?h.curv, ?h.sulc
Notes: 16
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 17
17
Upon Completion…
bert
scripts mri surf label stats
lh.aparc.annot
rh.aparc.annot
lh.aparc.a2009s.annot
rh.aparc.a2009s.annot
Desikan/Killiany Atlas
Destrieux Atlas
Notes: 17
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 18
18
Upon Completion…
bert
scripts mri surf label stats
aseg.stats – subcortical volumetric stats
wmparc.stats – white matter segmentation volumetric stats
lh.aparc.stats – left hemi Desikan/Killiany surface stats
rh.aparc.stats – right hemi Desikan/Killiany surface stats
lh.aparc.a2009.stats – left hemi Destrieux
rh.aparc.a2009.stats – right hemi Destrieux
stats files are text files with summary information, eg:
volume of left amygdala
average thickness in superior temporal gyrus
Notes: 18
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 19
Some of the Processing Steps…
19
Notes: 19

## Slide 20
Native Anatomical Space 1x1x1.1mm, 256x256x128, Sag
Conformed Anatomical Space 1x1x1mm, 256x256x256, Cor
“Anatomical Space”
orig.mgz
Surfaces
Parcellations
Segmentations
Conform Step
orig.mgz
mri
rawavg.mgz
bert
rawavg.mgz
20

## Slide 21
21
Talairach Transform
Computes 12 DOF transform matrix
Does NOT resample to Talaiarch space!
MNI305 template
Mostly used to report coordinates
transforms
talairach.xfm  text file with matrix
bert
scripts mri surf label stats
Notes: computes transformation matrix, using MNI305 template, not resampling – just transform
Tells FS how to get from anatomical space -> MNI space (contains talairach labels)
Montreal Neurological Institute
21

## Slide 22
22
Intensity Bias/Normalization
Outside of image is much brighter than inside (coils)
Worse with many coils
Makes gray/white segmentation difficult
Intensity Normalization (aka “Bias Correction”)
mri
T1.mgz
bert
Raw Data
Corrected (T1.mgz)
Notes: -Remove bias from the coil. brain areas closer to coil are brighter than others, get rid of bias.
-Hard to see with human eye, demonstrates map of intensity bias. Want to make it uniform.
-No coils in middle of brain (poorer SNR, CNR).
22

## Slide 23
23
Skull Strip
Removes all non-brain
  Skull, Eyes, Neck, Dura
brainmask.mgz (cf, brain.mgz)
T1.mgz
brainmask.mgz
brainmask.mgz
mri
bert
Notes: remove non brain areas, gives us brainmask (work with it a lot). Again, helps with wm/gm seg

## Slide 24
24
Automatic Volume Labeling
Used to fill in subcortical structures for creating subcortical mass
Useful in its own right
aseg.mgz
More in ROI Talk
ASeg Volume
aseg.mgz
mri
bert
Atlas:
$FREESURFER_HOME/average/RB_all_2016-05-10.vc700.gca
Notes: -Automatic segmentation (multi source of info), known intensity profiles, neighborhood relations, probability of voxel label given spatial location
-get stats for subcortical structures
Several papers on FS wiki detailing sub-cortical segmentation in FS
See ROI talk online, plus tutorial
24

## Slide 25
25
“Subcortical Mass” (filled.mgz)
Everything inside the cortical surface
  WM, most subcortical GM: putamen, pallidum, thalamus, caudate, ventral DC, most non-ventricular CSF.
  Excludes: hippocampus, brainstem, cerebellum, 3rd and 4th ventricles, parts of inferior lateral ventricles
Fills in any holes
Separates hemispheres (left=blue=255, right=green=128)
Notes: Final step: prepare for generating wm surf
Separate mask, one side per hemi, each hemi gets separate surface.
25

## Slide 26
26
“Subcortical Mass” (filled.mgz)
Proto surface
Still a volume
Editable
filled.mgz
mri
bert
Notes: Final step: prepare for generating wm surf
Separate mask, one side per hemi, each hemi gets separate surface.
26

## Slide 27
27
Surface Extraction
Fit to filled.mgz
1mm resolution
Rough, jagged
One for each hemisphere
filled.mgz
lh.orig.nofix
rh.orig.nofix
surf
bert
lh.orig.nofix
rh.orig.nofix
Notes: 27
-label all wm, fills in ventricles and other structures based on aseg. Mask to extract wm.
Ventricles are filled in (as are the other subcortical structures).
Set of histograms in axial/horizontal plane, highest peak in each histo near center of image classified as wm (most voxels), checks across slices to make sure classification consistent, centers wm intensities on 110.

## Slide 28
28
Surface Model
Mesh (“Finite Element”)
Vertex = point of triangles
Neighborhood
XYZ at each vertex
Triangles/Faces ~ 300,000
Vertices ~ 140,000
Area, Distance
Curvature, Thickness
Notes: 28
-mesh allows FS to get various measurements
-all triangles meet at various points called vertices – measurements stored there (area = area of all triangles)
-XYZ - each vertex has a label (important for cross-subject reg)
Once the xyz of each corner of each triangle is known, then it is possible to characterize the entire cortical surface in terms of area, distance, curvature, and thickness.
The cortical surface is represented by a finite element model using triangles to cover the cortical surface. The reconstruction is the (mostly automated) process of assigning an xyz to each corner of each triangle.

## Slide 29
29
Volume vs Surface Model
Volume
uniform grid
voxel is an intersection of grid lines
columns, rows, slices
voxel size/distance
voxel assigned a value
XYZ
Surface
NON-uniform grid
vertex is an intersection of triangles
each vertex has an index
distance between vertices ~1mm
vertex assigned a value
XYZ
Vector of vertex values (~140,000)
Notes: 29

## Slide 30
30
White Matter Surface
Nudge orig surface
Follow T1 intensity gradients
Smoothness constraint
Vertex identity preserved
orig surface
white surface
subject/surf/lh.white, rh.white
Notes: 30

## Slide 31
31
Pial Surface
Nudge white surface
Follow T1 intensity gradients
Vertex identity preserved
subject/surf/lh.pial, rh.pial
Notes: Use finalized wm as starting point, pial grow out from wm surf, find fall off of gm and CSF,
31

## Slide 32: Pial surf grows from white surf

## Slide 33
33
Non-Cortical Areas of Surface
Amygdala, Putamen, Hippocampus, Caudate, Ventricles, CC
?h.cortex.label
Notes: certain part of medial wall not included in any cortical measures. Filled in to create continuous surface, makes certain calculations easier
image of masked out area,
view in three different planes.
33

## Slide 34: Inflation: 2D Surface in 3D Space
34
White Surface
Pial Surface
Nudge vertices
No intensity constraint
See inside sulci
Used for sphere
Notes: 34

## Slide 35
35
Cortical Thickness
white/gray surface
pial surface
lh.thickness, rh.thickness
Distance between white and pial surfaces
One value per vertex
Surface-based more accurate than volume-based
mm
“Overlay”, “Heat map”
Notes: -Now that you have wm & pial surfs…get cort meas
-calculates cort thick, distance between vertices on wm and gm. blue dots are vertices (indicated by). dist from wm to gm, and gm to wm and takes average.
35

## Slide 36
36
Curvature (Radial)
Circle tangent to surface at each vertex
Curvature measure is 1/radius of circle
One value per vertex
Signed (sulcus/gyrus)
subject/surf/lh.curv, rh.curv
“Overlay”, “Red/Green”
Notes: -there is a curvature for pial surface and curvature for white surface at every vertex
Curvature = ratio , 1/radius of circle best matches what’s going on at each vertex in all directions
-indicates how curvy at each vertex (not sulcul depth).
How bumpy, nothing to do with sulci/gyri
36

## Slide 37
37
Surface-based Area and Volume
subject/surf/lh.area, lh.volume
Each vertex has an area (mean of triangles)
Each vertex has a thickness
Each vertex has a volume (~area*thickness)
Group Map-based analysis of area and volume
  Similar to Voxel-based morphometry (VBM)
Notes: 37

## Slide 38
38
Spherical Registration
Sulcal Map
Spherical Inflation
High-Dimensional
Non-linear
Registration to
Spherical Template
Atlas template is called “fsaverage”
More in surface-based analysis talk.
lh.sphere, rh.sphere
lh.sphere.reg, rh.sphere.reg
Notes: 38
main reason to use FS, this stage (important slide).
Now we have surfs that can be inflated, (a) inflate to sphere, (b) align to template, (c) then put subject back into original space.
Template = fsaverage (40 adults ranging in age), we do not recommend processing MRI datasets with subjects younger than 4/5 years of age. Atlas built using adult data, prior information related to intensities and structures not representative of younger populations. Pediatric atlas is in the works (Lilla).

## Slide 39
39
Automatic Cortical Parcellation
Fine-tune based on
individual anatomy
Spherical Atlas based on Manual Labeling
Map to Individual
Thru Spherical Reg
Note: Similar methodology to volume labeling
More in the Anatomical ROI talk
subject/label/{lh,rh}.aparc.annot
Annotation overlay
Notes: -subject aligned to spherical atlas, take labels from cortparc atlas and apply to individ subject, since anatomical boundaries are matched up.
not just throwing labels on there, using individual anatomy to fine tune labels.
39

## Slide 40
40
Surface Overlays
lh.sulc on inflated
lh.curv on inflated
lh.thickness on inflated
Value for each vertex
Color indicates value
Color: gray, red/green, heat, color table
Rendered on any surface
fMRI/Stat Maps too
lh.aparc.annot on inflated
lh.sulc on pial
lh.curv on inflated
fMRI on inflated
Notes: 40
Name some of them.
All surfaces have the same number of vertices. Different surfaces are made by moving the triangles around to achieve some goal. There is a one-to-one correspondence between surfaces which allows the user to cross-reference vertices from one surface to another (even across subjects) and to the volume. This feature is critical to get properly oriented. In the flat surface, there’s still a one-to-one correspondence, but not all vertices in the orig surface may be represented.

## Slide 41
41
Region of Interest (ROI) Summaries
$SUBJECTS_DIR /bert
scripts mri surf label stats
aseg.stats
lh.aparc.stats
rh.aparc.stats
wmparc.stats
…
Notes: 41
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 42
42
ROI Summaries:
Index SegId NVoxels Volume_mm3 StructName Mean StdDev Min Max Range
1 4 7230 7553.6 Left-Lateral-Ventricle 29.2 12.5 11.0 91.0 80.0
2 5 267 311.1 Left-Inf-Lat-Vent 51.3 11.5 14.0 84.0 70.0
3 7 10858 11506.0 Left-Cerebellum-White-Matter 86.8 6.7 24.0 106.0 82.0
4 8 50468 50270.0 Left-Cerebellum-Cortex 63.6 11.0 5.0 95.0 90.0
5 10 6625 6379.0 Left-Thalamus-Proper 91.6 8.8 40.0 111.0 71.0
6 11 3335 3407.1 Left-Caudate 81.2 7.1 50.0 100.0 50.0
7 12 4369 4385.7 Left-Putamen 87.2 5.2 57.0 106.0 49.0
8 13 1943 1923.6 Left-Pallidum 98.7 3.9 65.0 112.0 47.0
11 16 17918 17745.1 Brain-Stem 85.7 10.5 25.0 108.0 83.0
12 17 4014 3842.1 Left-Hippocampus 71.1 7.7 26.0 101.0 75.0
13 18 1598 1559.4 Left-Amygdala 72.8 6.4 27.0 97.0 70.0
aseg.stats – volume summaries
?h.aparc.stats – desikan/killiany surface summaries
?h.aparc.a2009s.stats – destrieux surface summaries
wmparc.stats – white matter parcellation
Routines to generate spread sheets for multiple subjects
asegstats2table --help
aparcstats2table --help
More info in Anatomical ROI talk.
Notes: Stats, subcortical from aseg, cortical from surfaces
Found in scripts dir
Have functions to compile individual subjects stats, select certain ROIs, or all.
42

## Slide 43
43
Overview
$SUBJECTS_DIR /bert
scripts mri surf label stats
recon-all –i file.dcm –subject bert –all
orig.mgz
lh.inflated
lh.aparc.annot
aseg.stats
recon-all.log
Notes: 43
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 44
44
Tutorial Tips
Do not run multiple instances of Freeview at the same time unless you have > 8GB RAM.
If you are running a command in the foreground, you should not type additional commands in that terminal (command prompt will be missing)
Right
Left
Volume Viewer (Freeview) Radiological Orientation
Note: Neurological Orientation available with 7.3
Notes: 44

## Slide 45: What to do next
Notes: Directions on where to get tutorial data & how to run recon-all on QuickInstall wiki

## Slide 46: Getting Answers
Mail Archive
46
Wiki
recon-all -help
mri_convert -help
$FREESURFER_HOME/docs
Send questions to:
freesurfer@nmr.mgh.harvard.edu
Notes: 46

## Slide 47
47
What is a "subject"?
What is the SUBJECTS_DIR?
What does it mean to conform the volume?
Are the FS results in Talairach/mni305 or native space?
What is the subcortical?
What is the medial wall?
Will the surface be accurate in the medial wall?
What is the difference between a surface and a surface overlay?
What does "?h" mean?
How do you get help?
Pop Quiz!
Notes: 47

## Slide 48
48
End of Presentation
Notes: 48

## Slide 49
49
Intensity Normalization
Removes B1 bias field
NU (MNI) nu.mgz
Presegmentation (T1.mgz)
  Most WM = 110 intensity
  Pre- and Post-Skull Strip
nu.mgz
mri
bert
T1.mgz
T1.mgz
nu.mgz
110.9 ±1.8
108.9 ±1.5
110.0 ±0.0
Notes: Nu volume created – bias removed
T1 – adjust intensity so that wm is around 110
Makes wm segment easier and generate wm surface
The B1 bias field is estimated by measuring the variation in the white matter intensity. The main body of the white matter is used to estimate the field across the entire volume. The intensity at each voxel is then divided by the estimated bias field at that location in order to remove the effect of the bias field.
Intensity = brightness of voxel – ideally only indicative of the MR params of the tissue (PD, T2, T1).
GM = dark, WM = bright.
Bias = changes in intensity across space that are unrelated to biology. i.e. tissue gets further away from receive coil, gets darker in intensity. When talking about bias, referring to biologically unrelated fluctuations in intensity.

## Slide 50
50
Results
Volumes
Surfaces
Surface Overlays
ROI Summaries
Notes: All organize in each subjects folder in SUBJECTS_DIR path
50

## Slide 51
51
Volumes
orig.mgz
$SUBJECTS_DIR/bert/mri
All “Conformed” 2563, 1mm3
Many more …
aseg.mgz
T1.mgz
brainmask.mgz
wm.mgz
filled.mgz
Subcortical Mass
aparc+aseg.mgz
Volume Viewer:
tkmedit
Notes: 51
Overview of main volumes created. most important ones brainmask, wm.mgz (editing, fix topos).
use tkmedit to view/edit

## Slide 52
52
Surfaces
orig
white
pial
inflated
sphere,sphere.reg
patch (flattened)
$SUBJECTS_DIR/bert/surf
Number/Identity of vertices stays the same (except patches)
XYZ Location Changes
Flattening not done as part of standard reconstruction
Surface Viewer:
tksurfer
Notes: 52
-All surfaces have the same number of vertices (within one subject??)
-There is a one-to-one correspondence between surfaces which allows the user to cross-reference vertices from one surface to another (even across subjects) and to the volume.
Different surfaces are made by moving the triangles around to achieve some goal. This feature is critical to get properly oriented. In the flat surface, there’s still a one-to-one correspondence, but not all vertices in the orig surface may be represented.

## Slide 53
53
Topological Defects
Fornix
Pallidum and Putamen
hippocampus
Ventricles and Caudate
Cortical Defects
Holes
Handles
Automatically Fixed
Notes: Examples of topo defects on surface which should be corrected.
-cut handles
-fill holes
53

## Slide 54
54
Subject Folder Directory Tree
bert
scripts mri surf label stats
orig.mgz T1.mgz brain.mgz wm.mgz aseg.mgz
recon-all –i file.dcm –subject bert –all
Notes: 54
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 55
55
Surface Reconstruction Overview
Input: T1-weighted (MPRAGE,SPGR)
Find white/gray surface
Find pial surface
“Find” = create mesh
  Vertices, neighbors, triangles, coordinates
  Accurately follows boundaries between tissue types
  “Topologically Correct”
    closed surface, no donut holes
    no self-intersections
Generate surface-based cross-subject registration
Label cortical folding patterns
Subcortical Segmentation along the way
Notes: 55

## Slide 56
56
Find “Subcortical Mass”
All White Matter
All Subcortical Structures
Ventricles
Excludes brain stem and cerebellum
Hemispheres separated
Connected (no islands)
Many Stages … More Later …
Notes: Overall goal, extract wm along with subcortical structures
After certain point hemis processed seperately
56

## Slide 57
57
MGZ File Format
001.mgz
mgz = compressed MGH file
Can store 4D (like NIFTI)
cols, rows, slices, frames
Generic: volumes and Surfaces
Eg, Typical Anatomical volume: 256 x 256 x 128 x 1
“Volume-encoded” Surface Files
nvertices, 1, 1, frames (eg, 163214 x 1 x 1 x 40)
No geometry information
lh.thickness.sm10.mgz
Notes: FS uses special file format (volumes FS creates in this format)
-do not need to convert dicom or nifti, FS does this (using mri_convert)
-A frame is the 4th dimension which is the variable you are analyzing. The first 3 dimensions are spatial and the fourth is the variable (schizophrenics vs. controls).
-analyze format is SPM format; “Siemens IMA” and AFNI is fmri software
57

## Slide 58
58
Other File Formats
Surface: Vertices, XYZ, neighbors (lh.white)
Curv: lh.curv, lh.sulc, lh.thickness
Annotation: lh.aparc.annot
Label: lh.pericalcarine.label
Unique to FreeSurfer
FreeSurfer can read/write:
  NIFTI, Analyze, MINC
FreeSurfer can read:
  DICOM, Siemens IMA, AFNI
Notes: Curv: surface overlay (stats visualized on surface)
Annot: surface label
Label: volumetric label
FS read and write variety of formats
58

## Slide 59
59
Fully Automated Reconstruction
Come back in 20 hours …
Check your results – do the white and pial surfaces follow the boundaries?
-- Can be broken up
Launch reconstruction:
recon-all –i file.dcm –subject bert –all
Where file.dcm is one file from the correct (T1-weighted)
MR series.
Notes: -all: perform all standard recon steps
-not so distant future, sig less time
-visually inspect results
Certain functions implemented using CUDA to take advantage of GPU
Collaboration with IBM to implement OpenMP versions of certain functions
59

## Slide 60
60
SUBJECTS_DIR Environment Variable
bert
$SUBJECTS_DIR
fred
jenny
margaret …
Subject
recon-all –i file.dcm –subject bert –all
Notes: 60
-Necessary to tell FS where your data, where to save output.
-Each unique subject has standard sub-directory heirarchy, organizes the output (volumes, surfs, logs, stats, etc.)

## Slide 61
61
FreeSurfer Directory Tree
bert
scripts surf label mri stats
orig.mgz T1.mgz brain.mgz wm.mgz aseg.mgz
Subject
Subject Name
Each data set has its own unique SubjectId (eg, bert)
recon-all –i file.dcm –subject bert –all
Notes: 61
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 62
62
Sulcal Depth
lh.sulc, rh.sulc
lh.curv, rh.curv
Notes: Distance vertex travel from wm/pial surface to ?h.inflated version.
Less detail than curv measure
?h.sulc (sulcal depth) used to register (grossly align) with atlas
?h.curv to tweak alignment to take individual anatomy into account.
Another cortical measure
Show to prove curv not sulcal depth
62

## Slide 63
63
Tessellation and Topology Fixing
Mosaic of triangles (“tessellation”)
Errors: Donut holes, handles
Automatic topology fixer
orig surface
surf/lh.orig
surf/rh.orig
Notes: lay mesh of triangles around wm.mgz,
-original guess(first draft) at wm surface, contains some errors (subsequently fixed)
-dont think as one slice, but over entire brain.
63

## Slide 64: Pial surf grows from white surf

## Slide 65
65
Motion Correction and Averaging
001.mgz
002.mgz
+
rawavg.mgz
orig
001.mgz 002.mgz
mri
rawavg.mgz
Does not change native resolution.
Usually only need one.
bert
Notes: FS dir structure illustrated on slides
Can give more than one, then avg to rawavg.
used to be that 2 acqs recommended, now with 3T, 32ch, MEMPRAGE, one recommended. still beneficial to collect to acquisitions, then use one with best contrast, one or 2, make sure it's consistent.
2 mprage at 1.5
1 mprage at 3t (SNR is good) - only use 1 or 2 for all subjects
-uses robust_register, no longer fsl
65

## Slide 66
66
Getting FreeSurfer
surfer.nmr.mgh.harvard.edu
  Register
  Download
  Mailing List
Wiki: surfer.nmr.mgh.harvard.edu/fswiki
Platforms:
  Linux
  Mac
  Windows (VirtualBox)
Installed in $FREESURFER_HOME

## Slide 67: Download & Install

## Slide 68
68
Overview
recon-all –i file.dcm –subject bert –all
Notes: Recon-all command
GUI – graphical user interface
Familiar with…
68

## Slide 69
69
Intensity Bias
Left side of the image much brighter than right side
Worse with many coils
Makes gray/white segmentation difficult
mri
T1.mgz
bert
Notes: -Remove bias from the coil. brain areas closer to coil are brighter than others, get rid of bias.
-Hard to see with human eye, demonstrates map of intensity bias. Want to make it uniform.
-No coils in middle of brain (poorer SNR, CNR).
69

## Slide 70
70
“White Matter” Segmentation
Separates white matter from everything else
Uses aseg to “fill in” subcortical structures
Cerebellum removed, brain stem still there
wm.mgz -- “wm” not a very good name!
wm.mgz
mri
bert
Notes: 70

## Slide 71
71
Fill and Cut (Subcortical Mass)
WM Volume (wm.mgz)
Filled Volume (filled.mgz)
(Subcortical Mass)
Fills in any holes.
Removes any islands
Removes brain stem
Separates hemispheres (each hemi has different value)
filled.mgz = “Subcortical Mass”
Notes: Final step: prepare for generating wm surf
Separate mask, one side per hemi, each hemi gets separate surface.
71

## Slide 72
72
Surface Extraction
Hemispheres separated
Fit to filled.mgz
1mm resolution
Rough, jagged
wm.mgz
lh.orig
rh.orig
surf
bert
lh.orig
rh.orig
Notes: 72
-label all wm, fills in ventricles and other structures based on aseg. Mask to extract wm.
Ventricles are filled in (as are the other subcortical structures).
Set of histograms in axial/horizontal plane, highest peak in each histo near center of image classified as wm (most voxels), checks across slices to make sure classification consistent, centers wm intensities on 110.